Important!

      - READ INSTRUCTIONS COMPLETELY BEFORE COLLECTING YOUR SAMPLES.

      - Collect your samples ONLY on the collection day you have been assigned.

- Do not remove caps from sample bottles until you are ready to take each sample. Fill each of the 4 sample bottles and replace each cap one at a time.

- Sample collection instruction VIDEO is found here: http://bit.ly/1UGZkxo.

Instructions:

- In order to test for metals (lead and copper) that might be in your plumbing system, the water will need to remain in the pipes for at least 6-8 hours.  The night before your scheduled collection day, do not use any water after 10 pm.

- Collect the samples first thing in the morning, before any water has been used anywhere in the house.  Choose a cold water faucet in the kitchen or bathroom.  Be sure that the sink is clean, and that all dishes and other items are removed in order to minimize splashing.  If you drink your water, and want to know about the quality of the water you drink, collect from the faucet where you obtain this water.  Do not remove the aerator on the faucet.

- Find the bottle labeled FIRST (with an “X” on the cap) and carefully remove the cap, taking care not to touch the inside of the cap or sample bottle.  Do not remove the cap from more than one bottle at a time.  Do not put the cap down while collecting the sample.

- Holding the “FIRST” bottle under the faucet, turn the water on, opening the handle as far as you normally would, and fill the bottle completely.  Leave as little air as possible in the bottle, without letting the water overflow. Replace cap when full.

- While the water is running, wash your hands thoroughly to ensure there is no cross-contamination of the bacteria samples.  Allow the water to run at least 1 minute to flush out the pipes.

- One at a time, fill the remaining three sample bottles to the top, holding each cap in your hand while you fill the bottle, and taking care not to touch the inside of the caps or the bottles. Leave as little air as possible in each bottle.  After filling each bottle, replace and tighten the cap securely.  Repeat with the remaining bottles.

- Do not write on the sample bottles.

- Store samples in refrigerator or on ice.

- Complete the Drinking Water Clinic Questionnaire and bring it, with all 4 water sample bottles, to the designated collection site at the designated time on your collection day.  PLEASE KEEP QUESTIONNAIRE DRY AND SEPARATE FROM BOTTLES.